## Slide 1
*.control.inp
0.5e-06 0.3 0. 1.4e-04 'dt w alpha beta (Rayleigh)'
0.3 50. 1000 50 10 'tmax, amplification factor, pfreq, pfreq2,pfreq3 '
1 'number of materials '
35.7e09 2400. 0.000125 5. 20. 100. 0.6 0.2 0.005 'Ec rho epscr a1 a2 a3 b1 b2 dsize '
0 200e09 0.002625 0.1 550.0e06 'steelflag Es ey eult sult '
1 'read acc file 0/1'
'acc2.inp' 0.0 'acc file acc multiplier'
1 'number of existing cracks'
-0.1 0.775 0.361 0.775 1.0 'x1 y1 x2 y2 strainm for the crack'
0 'read damage data - inactive '
dt , w, alpha, beta
ttmax, amp, pfreq, pfreq2, pfreq3
nmaterials
a1(i), a2(i), a3(i), b1(i), b2(i), dsize(i)
steelflag, ey, eult, sult
readacc
accfile, accmult
ncracks
xlevel1(i), ylevel1(i), xlevel2(i), ylevel2(i)
readdamage
Newton, meter, second
multiple mateials/mass matrix is inactive
readdamage is inactive
steel/concrete -> elastoplastic
pfreq-> print frequency for spatial distribution files
pfreq2-> print frequency for screen info
pfreq3-> print frequency for temporal variation files
Red color: Integer
Black color: real
Blue color: String

## Slide 2
*.mesh.inp
1347 17343 3.29828202000000 5.000000000000000E-002 number of nodes, elements, area, dx
1 9.999999974752427E-007 -0.149999000000002 0 dummy integer, x(1), y(1)
2 9.999999974752427E-007 -9.999900000000250E-002 0 dummy integer, x(2), y(2)
3 9.999999974752427E-007 -4.999900000000246E-002 0
.
.
1 1 2 0 0.0 1 dummy integer, node 1, node 2, steel indicator, steel area, material type
2 1 3 0 0.0 1
3 1 4 0 0.0 1
nn , nel, area, dx
dummy, xcoord(i,1), xcoord(i,2)
.
.
.
dummy, elnode(i,1), elnode(i,2), steel(i), As(i), eltype(i)
Starts with node 1 and ends with node nn
Starts with element 1 and ends with element nel
Not all components of multiple materials work at this time

## Slide 3
*.boundary.inp
1 4 1 0 0 1 node number 1, node number 2, increment, support condition (0 fixed, 1 free), 0 (stop) / 1 (continue)
8 11 1 0 0 1
48 51 1 0 0 1
103 106 1 0 0 1
158 161 1 0 0 1
213 216 1 0 0 0
1 If boundaries are moving (1), if not (0) (following lines are not read when it is set to 0)
-0.01 2 velocity, direction
102 102 1 1 node number 1, node number 2, increment, 0 (stop) / 1 (continue)
157 157 1 1
212 212 1 1
267 267 1 1
322 322 1 0
If boundaries are moving, do not list the same degree of freedom in both NF and NFM lists
In this version, boundaries can only move in x- and y-directions
If you set fixed boundaries, the rest of the input file is not read.
Use ‘force-controlled’ simulation option in *.loading.inp
Typically, this will not work together with time-dependent loads so set them to zero or remove them from *.loading.inp
Support reactions calculated in the output files do not include the forces applied at degrees of freedom in the NFM list.
NF LIST
NFM LIST

## Slide 4
*.output.inp
3 'number of regular (time variation) monitor points '
102 1 1 'monitor point node number, direction (x->1, y->2), displacement ->1, velocity->2, acceleration->3'
102 1 2
102 1 3
2 'number of relative monitor points'
27 -26 2 2 ‘monitor point node number 1, node number 2, direction, disp/vel/acc’
27 -26 2 1
2 'number of graphs as a function of support reactions'
-1 5 ' -+support reaction and monitor number -> in this case -Rxn in x direction
2 1 and relative displacement of node 27 (y direction) with respect to node 26
nmonitor
monitor(i,1), monitor(i,2), monitor(i,3)
nmonitor2
monitor2(i,1), monitor2(i,2), monitor(i,3), monitor(i,4)
nbase
base(i,1), base(i,2)
For regular monitor points (nmonitor), negative sign shouldn’t be used
For relative monitor points (nmonitor2), negative/positive signs can be used arbitrarily
files m1.txt., m2.txt, m3.txt…. are opened and their order is taken from this file. This order is used or B1.txt, B2.txt files as well.
For example, velocity in x-direction for node 102 as a function of time is in file m2.txt.
Total support reactions in x and y directions are used in files B1.txt, B2.txt… (nbase).
If negative sign is used, -support reaction is written.
The second index (base(i,2)) is the monitor variable given above

## Slide 5
*.loading.inp
externalloadtype,nvcont1,nvcont2,vdesired,lambda
İgravity
gravity,tphase1,gravityacclimit
2 4 2 0.005 4.0e10 'force controlled 1 velocity controlled 2, monitor no, loading number, vdesired, lambda'
0 'gravity loading 0->no phase, 1-> phase for gravity'
0. 0.02 0.001 'gravitational acceleration, phase1end (second), maxacc (m/s^2)
When force controlled (externalloadtype=1) option is selected, rest of the variables in the first line are not used in the simulations
If velocity controlled (externalloadtype=2) option is selected, then rest of the variables in the first line are used in the control of the force
  nvcont1 : the monitor number (see *.output.inp file for information) that will be used to control the force (it should be either absolute or relative velocity)
  nvcont2 : number of the loading scenario (only a single loading scenario can be used)
  lambda: lambda is a rate parameter (N/m). Its choice will determine how fast force will be adjusted to keep velocity near the desired value
If igravity=1, a gravity loading phase is run during which gravitational acceleration is increased linearly from 0 to its original value g (t from 0 to phase1end.
Phase 1 ends after phase1end is reached and maximum acceleration in the system is less than gravityacclimit
If igravity=0, then phase 2 is run. If g is not equal to zero, weight is also taken into account.

## Slide 6
*.loading.inp continue
nloads
i1,i2,i3,i4,i5 -> uniform
i1,i2,i3,i5 -> triangular
tri(i,1),trif(i,1),tri(i,2),trif(i,2),trif(i,3),trif(i,4) -> triangular
loadingvalue(i,k,1),loadingvalue(i,k,2),i5
…
2 'number of different loadings '
1 '1 uniform 2 triangular 3 originating from a specified point'
94 102 1 1 0 'node i, node j, increment, direction, 0 stop 1 continue'
0.0 0.0 1 't1 f1 1/0'
0.001 0. 1
0.002 0. 0
2
5 7 1 1
15 47 1 1
88 102 1 0
5 1. 102 0. 1. 0.
0.0 0.0 1
0.01 10000. 1
0.015 10000. 1
0.020 0. 0
Provide force not force/length or force/area
Continous input for nodes or force(t) can be provided using the control integer at the end of the line (1=continue, 0=stop)
For uniform loading direction will be either x or y direction whereas for triangular loading, direction is in the unit vector direction (trif(i,3), trif(i,4))
Triangular loading also works for trapezoridal loads/uniform loads
trif(i,1) and trif(i,2) are not magnitudes, they are representative of force ratios.
Take, for example, the larger force trif(i,1) = 1 and smaller trif(i,2)=0.5 . It becomes a trapezoidal loading. If you take trif(i,2)=0, it becomes a triangular loading.
tri(i,1)
tri(i,2)
trif(i,1)
trif(i,2)
Unit normal
= (trif(i,3),trif(i,4))

## Slide 7
Output Files
Only temporal files are written in the gravitational loading phase
The text ‘zzz’ is replaced by the time step number for spatial distribution files
m1.txt, m2.txt, m3.txt… : monitor files (functions of time)
b1.txt, b2.txt…: monitor values as a function of support reactions
rxn1.txt, rxn2.txt: support reactions as a function of time
strainzzz.txt: strain for undamaged elements
allzzz.txt: strain for all elements
strainmzzz.txt, stpzzz.txt: maximum strain for elements (with damage)
damagezzz.txt: a measure of damage for nodes (1 intact, 0.5 fractured, 0 unattached
uxzzz.txt, uyzzz.txt: displacement field
vxzzz.txt, vyzzz.txt: velocity field
accxzzz.txt, accyzzz.txt: acceleration field
uuuzzz.txt, vvvzzz.txt: magnitude of displacement and velocity vectors